State preparation
for quantum tunneling

---
Quantum Tunneling: Initial state
It must be localized in a specific region, |x>.
Its kinetic energy, |k>, should not exceed the maximum value of potential barrier, otherwise it becomes classic or mixed state.
V0
\langle K \rangle < \langle V \rangle
|\psi_0\rangle
|\psi_0\rangle

---
Quantum Tunneling: Initial state
Procedure
(|k>) State preparation to fullfill<K> < V-e.
Apply QFT - (|k> → |x>)
Add a qubit to the register, (n → n+1)

---
Quantum Tunneling: Localization(|x>)
Additional qubit to the register, (n → n+1)
Arbitrary state on position space
| \psi \rangle_{n+1}
|0\rangle
| \psi \rangle_{n+1} = | \psi \rangle_{n} \otimes | x \rangle
\left\{ \right.
\frac{1}{\sqrt{2}} (|0 \rangle + | 1 \rangle)
|1 \rangle
\langle \mathbf{x} |\psi\rangle_{n}
\langle \mathbf{x} |\psi\rangle_{n+1}

---
Quantum Tunneling: Localization(|x>)
A: A preparation directly corresponding to a specific position and <K> requires significant much costs to fullfill the requirements.
Why arbitrary shape?
The left is an inverse transformed state of a specific |k> state, which we can prepare easily, comparing to the above.
\langle \mathbf{x} |\psi\rangle_{n}

---
Quantum Tunneling: Localization(|x>)
| \psi \rangle_{n+1} |0\rangle |\psi\rangle_{n} \left\{ \right. \left\{ \right.
Upre
|\psi\rangle_{n}
| \psi \rangle_{n+1}

---
Quantum Tunneling: Localization(|x>)
Upre
Uk,pre
QFT
See further references for a general distribution implementation
on the amplitude of states.
However, some state can be encoded with simple X, H gates.
Dasgupta, Paine, arXiv:2208.13372
Uk,pre
|\psi\rangle_{n}
\left\{ \right.

---
Quantum Tunneling: Localization(|x>)
| \psi \rangle_{n+1} |0\rangle |\psi\rangle_{n} \left\{ \right. \left\{ \right.
U
\langle K \rangle < \langle V \rangle
|\psi\rangle_{n}
| \psi \rangle_{n+1}

---
Quantum Tunneling: Energy expectation value
Energy expectation value
Q
?
\langle K \rangle_n < V_0
|\psi\rangle_{n}
| \psi \rangle_{n+1} = | \psi \rangle_{n} \otimes | x \rangle
\langle K \rangle_{n+1} < V_0

---
Quantum Tunneling
Momentum Operator n+1
. . .
0
1
2
3
4
5
k
\mathbf{\hat{P}}|_p = \frac{2 \pi}{2^{n+1}}\left(\sum_{j'=0}^{2^{n}} j' | j' \rangle \langle j' | + \sum_{j'=2^{n} + 1}^{2^{n+1}-1} (2^{n}- j' )| j' \rangle \langle j' | \right)
| k \rangle (- \hat{x})
| k \rangle (+ \hat{x})

---
Quantum Tunneling
Momentum Operator n-extended
. . .
0
1
2
3
4
5
k
\mathbf{\hat{P}}|_{p, n} \otimes \mathbf{I}
| k \rangle (- \hat{x})
| k \rangle (+ \hat{x})
\mathbf{\hat{P}}|_p = \frac{2 \pi}{2^n}\left(\sum_{j=0}^{2^{n-1}} j | j \rangle \langle j | + \sum_{j=2^{n-1} + 1}^{2^{n}-1} (2^{n-1} - j )| j \rangle \langle j | \right)

---
Quantum Tunneling
Momentum Operators
. . .
0
1
2
3
4
5
7
| k \rangle (- \hat{x})
\mathbf{\hat{P}}|_{p, n} \otimes \mathbf{I}
\mathbf{\hat{P}}|_{p, n+1}
| k \rangle (+ \hat{x})

---
Quantum Tunneling
Expectation Values
when
The above inequality becomes reversed when
\langle \psi |\mathbf{\hat{P}|_{p, n}} | \psi \rangle_{n} = \langle \psi |\mathbf{\hat{P}|_{p, n}} \otimes \mathbf{I} | \psi \rangle_{n+1}
\langle \psi |\mathbf{\hat{P}|_{p, n}} | \psi \rangle_{n} = \langle \psi |\mathbf{\hat{P}|_{p, n}} \otimes \mathbf{I} | \psi \rangle_{n+1}
|\psi\rangle_{n} = \sum_{k=0}^{2^n-1} \lambda_k | k \rangle
\, \lambda_k = 0, \, k > 2^{n-1}
\langle \psi |\mathbf{\hat{P}|_{p, n}} \otimes \mathbf{I} | \psi \rangle_{n+1} \leq \langle \psi | \mathbf{\hat{P}}|_{p, n+1} | \psi \rangle_{n+1}
\, \lambda_k = 0, \, k > 2^{n-1}
\lambda_k =0, k < 2^{n-1}

---
Quantum Tunneling
Expectation Values
The above term becomes “e” in the kinetic energy threshold.
\langle \psi | \mathbf{\hat{P}}|_{p, n+1} | \psi \rangle_{n+1} = \sum_{k=0} [ \lambda_{2k}^2 2k + \lambda_{2k+1}^2 (2k+1) ]
\langle \psi | \mathbf{\hat{P}}|_{p, n} \otimes \mathbf{I} | \psi \rangle_{n+1} = \sum_{k=0} [ \lambda_{2k}^2 + \lambda_{2k+1}^2 ] 2k
\Delta <K>_{n \rightarrow n+1} = C \sum_{k=0} \lambda_{2k+1}^2 (4k +1)
\, \lambda_k = 0, \, k > 2^{n-1}